## Slide 1
Segmenting individual nuclei
and auditing the benchmark that scores it
Tejas Sukesh
BBBC039 · 200 fields · 23,617 hand-annotated nuclei
Notes: I'll spend most of this on what the model gets wrong and why, because that turned out to be more interesting than the score.

## Slide 2
1
The task
Notes: 200 images, about 118 nuclei each. Draw a line around each one separately, and score it against outlines a human drew by hand. The hard part is telling apart nuclei that touch. Ten seconds. Move on.

## Slide 3
2
The trap in the data
The masks are a 3-colour graph colouring, not instance IDs
3
read as IDs
100
binarise + label
118
decoded correctly
Notes: The answer files look like they label each nucleus with its own ID. They don't — they only use three values, arranged so touching nuclei never share one. Take the pixel value as the object ID and the whole field collapses to three objects. Binarise and run connected components instead — the careful next guess — and every touching clump still fuses: 100 instead of 118 in this field. Either way your score goes UP, because the hard cases disappear from the test. I checked my decoding two ways: it recovers 23,617 objects, matching what the dataset documentation reports, and the count is identical under 4- and 8-connectivity.

## Slide 4
3
What I built
Notes: I used a pretrained model for the segmenting, and wrote a classical pipeline from scratch as a comparison. The piece that mattered most was a cache: testing a setting took 8.8 seconds per image, and I got it to 0.11 — about 72× faster, with byte-identical output. That's the median-based figure; the mean says 81×, but the first call includes loading the checkpoint, so 72× is the honest one. Everything after this depends on it. Pre-empts 'did you just call a library.' Don't be defensive, just state it.

## Slide 5
4
The number
0.791
mean AP over IoU 0.50 : 0.05 : 0.95 · held-out test set, 50 fields
95% CI 0.766 – 0.812
the spread that matters
F1 = 0.956
at the loosest threshold
mean IoU 0.926
over matched objects
Notes: That's the headline. But it's an average of ten increasingly strict judgments, and it's worth asking where it's actually losing points. Deliberately anticlimactic. You're setting up the pivot.

## Slide 6
5
Where the score is actually lost
The two strictest thresholds cause 54% of the total loss
Notes: At the loosest setting, it finds 93% correctly. At the strictest, 31%. The two strictest settings cause 54% of the total loss. Everything else — every missed object, every wrongly merged pair — is under 4% of it. So if I want to improve the number, that's where it lives. This is the pivot slide. Everything before was setup. Slow down here.

## Slide 7
6
What are those strict thresholds measuring?
Two reasonable definitions of “where the edge is” rank the outlines oppositely
Notes: To score at that strictness your outline must match the human's to within about half a pixel. So I asked whether a hand tracing is even that precise, using the image itself as a referee — two different definitions of where an edge is. They give opposite answers. Brightness-halfway favours the human in 67% of fields; edge-steepness favours the model in 96%. And the gradient measure is the one to weight, because it's reference-free — both outlines are divided by the same local contrast, so any calibration error cancels. The half-maximum measure needs 0.5 to be correctly located, and on this data it isn't: both outlines read about 0.40, not 0.50. Two reasonable definitions ranking them oppositely is itself the evidence that those strict thresholds are settling a convention rather than measuring correctness. Do NOT claim the annotation is wrong. Go straight to the next slide.

## Slide 8
7
I got this wrong first
Synthetic sweep with a known right answer: ground truth exactly on the edge, prediction 0.25 px too large
my first version
inner-boundary ring
9 of 9
picked the wrong outline
after the fix
marching-squares contour
0 of 9
picked correctly
The original claim reported the model closer in 48 of 49 fields. It did not survive. I retracted it.
Notes: My first version of this said the model was closer, in 48 of 49 images. Someone suggested that might be an artifact of how I sampled pixels along each outline. So I built a test with a known right answer — human's outline exactly on the edge, model's slightly outside it — and my measurement picked the wrong one nine times out of nine. I'd been sampling the ring of pixels just inside each outline, which sits half a pixel in, the same size as the effect. And it isn't common-mode: it favours whichever outline is larger, which is the model's. So the artifact alone could have produced the entire original result. I fixed the sampling, re-ran, and my headline finding inverted. So I retracted it. This is the best slide in the deck. Don't rush it.

## Slide 9
8
What actually fails
One population: small and faint
Notes: Setting the boundary question aside — of the objects it genuinely misses, the median is 20 pixels against 622 for a normal nucleus. 81% are under 100. Above 400 pixels it misses 9 out of 4,773, which is 0.2%. And the model finds 98% of bright objects but only 86% of faint ones. So it's one population: small and faint.

## Slide 10
9
Are those even objects?
I couldn’t answer that from a table, so I looked
Notes: There's a transition. Under about 15 pixels the annotation sits on visually empty background — that's label noise. Between 20 and 100 they're real but very faint. Above 100 they're unmistakable nuclei the model genuinely got wrong. So I can't dismiss the misses as bad labels, and I can't dismiss them as model failures either. Both are present.

## Slide 11
10
Six experiments, five null
Each was motivated by a measurement, and each failure eliminated a cause
What I tried | What it ruled out
Threshold tuning | Defaults already optimal
Size filter | Admits more noise than signal
Bandit search | Lost to brute force — my own speedup removed the need
Averaging flipped copies | Errors are consistent, not random
2× upscaling | Small objects aren’t a resolution problem
Local brightness rebalancing | Faint objects are faint absolutely, not relatively
Notes: Each of these was motivated by a measurement, and each failure eliminated a cause. The score didn't move — but I know why for every one. The bandit one is the embarrassing one, and worth owning: bandits exist to save evaluations, and my own 72× cache made evaluations cheap enough that brute force won. I killed the premise myself.

## Slide 12
11
The one that broke its prediction
I wrote down what I expected before running it. The opposite happened.
Merges
predicted: unchanged
103 → 69
dropped by a third
Misses under 50 px
predicted: recovered
265 → 266
did not move at all
Resolution isn’t why small objects are missed — and merging isn’t the immovable problem I’d argued it was.
AP stayed flat (0.807 → 0.809) because it traded merges for splits. The error profile changed substantially — visible only because those are counted separately.
Notes: I wrote down what I expected before running the last one: upscaling would recover small objects and leave merges alone. The opposite happened. Small objects didn't move at all — 265 to 266. But merges dropped by a third, 103 to 69. So resolution isn't why small objects are missed, and merging isn't the immovable problem I'd argued it was. The score stayed flat because it traded merges for splits — 24 splits up to 36 — but the error profile changed substantially, and I could only see that because I count those separately. CLOSING LINE: The score is roughly where a pretrained model puts it, and I couldn't move it. What I have instead is a map of which errors are reachable, which are definitional, and which are noise — and I can tell you which is which.

## Slide 13
B1
Did the model see this data?
Raise it yourself if it comes up naturally — it reads as rigour
Cellpose-SAM's training corpus includes the 2018 Data Science Bowl.
BBBC039's own dataset page states some of its images appear in that collection.
So the test score is not cleanly held out, and I don't claim it is.
It does not affect the failure analysis, which is about error structure, not rank.

## Slide 14
B2
The classical pipeline
Why opposite error types must be counted separately
 | Cellpose | Classical
Mean AP | 0.807 | 0.555
Splits | 24 | 405
Merges | 103 | 169
Object-count bias | −4.51% | −0.19%
Best object count in the project — achieved by making 574 topology errors that cancel. A count-only metric would rank it first.
Validation split

## Slide 15
B3
Worst cases
Chosen by sorting the per-image results, never by eye
figures/worst_cases/ holds all four

## Slide 16
B4
Per-image spread
Why every number carries a confidence interval

## Slide 17
B5
Merge composition
60% of “merges” are a nucleus plus a speck, not two nuclei fused